## Slide 1
North-South miscentering of the Jason-3 orbit observed by its yaw-flip capability
Eléonore Saquet, Alexandre Couhert, Flavien Mercier
Ocean Surface Topography Science Team Meeting
Precise Orbit Determination Splinter

## Slide 2: Introduction
Context
Previous approaches
Normal offset (GPS int ambiguity)
Flips approach (GPS int ambiguity)
Normal offset (other measurements)
Flips approach (other measurements)
Conclusion
OSTST 2020

## Slide 3: Context
OSTST 2020
Satellite: Jason-3
Nominal orientation: nadir Earth-pointed
Attitude law:
  Yaw steering when β’>15° and β’<-15°
  Fixed yaw when -15°<β’<15°
  A yaw flip is performed at β’=0°
Yaw flip benefits:
  Disentangle time tagging from along-track center of phase POD instrument offsets
  Observe separately the combined effects of cross-track miscalibrated SRP models/thermal effects or POD instrument locations, and the Z-component of geocenter motion whose amplitude is thoroughly debated

## Slide 4: Context
OSTST 2020
Goal:
Monitoring of the residual normal perturbations
Observation of the geocenter motion estimates in the Z (North-South) direction
  Comparison with previous methods
Approach:
Focus on orbit arcs where flip events occur
Definition of the 8-day orbit arcs: 4 days before and after the flip events
Estimated empirical parameters:
  constant cross-track accelerations with 4-day intervals
  periodic once-per-revolution accelerations in the along/cross-track directions with 1-day intervals
  constant along-track accelerations with 2 orbital period intervals

## Slide 5: Context
OSTST 2020
Normal acceleration offset before and after the flip caused by:
  Cross-track error in the POD center of phase location
  Residual SRP modeling error of the satellite normal surfaces
  Unmodeled satellite thermal effects
Common normal acceleration bias on both sides of the flip caused by:
  Geocenter motion in the Z direction (mainly)
  Residual solar-reflected/Earth-emitted radiation modeling errors?
The miscentering of the orbit around the Earth’s CM in the Z direction can be recovered using the equation:
where is the common cross-track acceleration bias
Normal acceleration offset
Common normal acceleration bias

## Slide 6: Previous approaches
Approach | 365-day Amplitude | Phase
GPS+J3 (flt. amb., Couhert et al., 2020) | 7.7 mm | 361 d
GPS+J3 (int. amb., Couhert et al., 2020) | 5.0 mm | 24 d
DORIS+J3 (Couhert et al., 2018) | 4.4 mm | 23 d
OSTST 2020

## Slide 7: Normal offset (GPS int. ambiguity)
OSTST 2020
Offsets of the estimated normal accelerations before/after the flip (the common bias has been removed), which can be attributed to a wrong cross-track center of phase/mass location. The correction to be applied is given by:
GPS measurements: integer ambiguity
2
Nota: the two groups of colors (blue/orange) denote the forward and backward flying attitude regimes

## Slide 8: Normal offset (GPS int. ambiguity)
Decrease in the 118-day signal of the previous approaches, when applying the normal offset correction (via the GPS antenna phase center)
Approach | 365-day Amplitude | Phase
GPS+Jason-3 (int. amb., Couhert et al., 2020) | 5.0 mm | 24 d
GPS+Jason-3 corr (int. amb., Couhert et al., 2020) | 5.0 mm | 24 d
OSTST 2020

## Slide 9: Flips approach (GPS int. ambiguity)
OSTST 2020
Approach | 365-day Amplitude | Phase
GPS+Jason-3 (int. amb., Couhert et al., 2020) | 5.0 mm | 24 d
Flips (GPS int. amb.) | 2.9 mm | 48 d
Common normal acceleration biases estimated on both sides of the flips reflecting the North-South miscentering of the Jason-3 orbit

## Slide 10: Normal offset (other measurements)
GPS measurements: float ambiguity
DORIS measurements
The observability of these measurements in the cross-track direction is not strong enough
OSTST 2020

## Slide 11: Flips approach (other measurements)
OSTST 2020
Approach | 365-day Amplitude | Phase
Flips (DORIS) | 9.3 mm | 52 d
Flips (GPS flt. amb.) | 5.5 mm | 331 d

## Slide 12: Conclusion
OSTST 2020
The flips approach allows us to observe specifically the geocenter motion along the Z (North-South) axis.
The 60-day sampling and/or residual errors in the modelling of solar-reflected/Earth-emitted radiations could explain the differences in the annual TZ geocenter estimates between the flips and previous approaches.
Yaw flips are specific to the T/P and Jason missions. A recommendation of the OSTST POD group is to maintain the yaw flips for the Sentinel-6/Jason-CS mission.